## Slide 1
Module 9: Firewall Technologies
Networking Security v1.0
(NETSEC)
Notes: Networking Security (NETSEC) Module 9: Firewall Technologies

## Slide 2: Module Objectives
Module Title: Firewall Technologies
Module Objective: Explain how firewalls are implemented to provide network security.
Topic Title | Topic Objective
Secure Networks with Firewalls | Explain how firewalls are used to help secure networks.
Firewalls in Network Design | Explain design considerations for implementing firewall technologies.
Notes: 2
1 – Networking Today
1.0.2 – What will I learn to do in this module?

## Slide 3
9.1 Secure Networks with Firewalls
Notes: 9: Firewall Technologies 9.1: Secure Networks with Firewalls

## Slide 4
Secure Networks with Firewalls
Firewalls
All firewalls share some common properties:
Firewalls are resistant to network attacks.
Firewalls are the only transit point between internal corporate networks and external networks because all traffic flows through the firewall.
Firewalls enforce the access control policy.
Different types of firewalls have different benefits and limitations.
Notes: 9: Firewall Technologies 9.1: Secure Networks with Firewalls 9.1.1: Firewalls

## Slide 5
Secure Networks with Firewalls
Types of Firewalls
It is important to understand the different types of firewalls and their specific capabilities so that the right firewall is used for each situation.
Packet Filtering (Stateless) firewalls - These are usually part of a router firewall, which permits or denies traffic based on Layer 3 and Layer 4 information. They are stateless firewalls that use a simple policy table look-up that filters traffic based on specific criteria.
Stateful firewalls – These are the most versatile and the most common firewall technologies in use. Stateful firewalls provide stateful packet filtering by using connection information maintained in a state table. Stateful filtering is a firewall architecture at the network layer.
Application Gateway (Proxy) firewalls – These filter information at Layers 3, 4, 5, and 7. Most of the firewall control and filtering is done in software. When a client needs to access a remote server, it connects to a proxy server.
Next Generation firewalls – These go beyond stateful firewalls by providing integrated intrusion prevention, application awareness and control, upgrade paths to include future information feeds, and techniques to address evolving security threats.
Notes: 9: Firewall Technologies 9.1: Secure Networks with Firewalls 9.1.2: Types of Firewalls
9.1.3: Check Your Understanding – Identify the Type of Firewall

## Slide 6
Secure Networks with Firewalls
Packet Filtering Firewall Benefits and Limitations
Benefits of Packet Filtering Firewalls:
They implement simple permit or deny rule sets.
They have a low impact on network performance.
They are easy to implement and are supported by most routers.
They provide an initial degree of security at the network layer.
They perform many of the tasks of a high-end firewall at a much lower cost.
Limitations of Packet Filtering Firewalls:
They are susceptible to IP spoofing.
They do not reliably filter fragmented packets.
They use complex ACLs, which can be difficult to implement and maintain.
They cannot dynamically filter certain services.
They are stateless.
Notes: 9: Firewall Technologies 9.1: Secure Networks with Firewalls 9.1.4: Packet Filtering Firewall Benefits and Limitations

## Slide 7
Secure Networks with Firewalls
Stateful Firewall Benefits and Limitations
Benefits | Limitations
Primary means of defense | No Application Layer inspection
Strong packet filtering | Limited tracking of stateless protocols
Improved performance over packet filters | Difficult to defend against dynamic port negotiation
Defends against spoofing and DoS attacks | No authentication support
Richer data log | 
The table lists benefits and limitations of stateful firewalls.
Notes: 9: Firewall Technologies 9.1: Secure Networks with Firewalls 9.1.5: Stateful Firewall Benefits and Limitations

## Slide 8
9.2 Firewalls in Network Design
Notes: 9: Firewall Technologies 9.2: Firewalls in Network Design

## Slide 9
Firewalls in Network Design
Common Security Architectures
Firewall design is primarily about device interfaces permitting or denying traffic based on the source, the destination, and the type of traffic. Here are three common firewall designs:
  Private and Public
  Demilitarized Zone (DMZ)
  Zone-Based Policy
Notes: 9: Firewall Technologies 9.2: Firewalls in Network Design 9.2.1: Common Security Architectures

## Slide 10
Firewalls in Network Design
Common Security Architectures (Cont.)
Private and Public - The public network (or outside network) is untrusted, and the private network (or inside network) is trusted.
Notes: 9: Firewall Technologies 9.2: Firewalls in Network Design 9.2.1: Common Security Architectures

## Slide 11
Firewalls in Network Design
Common Security Architectures (Cont.)
Demilitarized Zone (DMZ) - This is a firewall design where there is typically one inside interface connected to the private network, one outside interface connected to the public network, and one DMZ interface.
Notes: 9: Firewall Technologies 9.2: Firewalls in Network Design 9.2.1: Common Security Architectures

## Slide 12
Firewalls in Network Design
Common Security Architectures
Zone-Based Policy - Zone-based policy firewalls (ZPFs) use the concept of zones to provide additional flexibility. A zone is a group of one or more interfaces that have similar functions or features. Zones help you specify where a Cisco IOS firewall rule or policy should be applied.
Notes: 9: Firewall Technologies 9.2: Firewalls in Network Design 9.2.1: Common Security Architectures

## Slide 13
Firewalls in Network Design
Layered Defense
A layered defense uses different types of firewalls that are combined in layers to add depth to the security of an organization. Policies can be enforced between the layers and inside the layers. The following example shows four layers of security.
Network Core security - Protects against malicious software and traffic anomalies, enforces network policies, and ensures survivability
Perimeter security - Secures boundaries between zones
Communications security - Provides information assurance
Endpoint security - Provides identity and device security policy compliance
Notes: 9: Firewall Technologies 9.2: Firewalls in Network Design 9.2.2: Layered Defense
9.2.3: Check Your Understanding – Identify Basic Security Architecture for Firewalls

## Slide 14
Firewalls in Network Design
Layered Defense (Cont.)
This partial list of best practices can serve as a starting point for a firewall security policy.
Position firewalls at security boundaries. Firewalls are a critical part of network security, but it is unwise to rely exclusively on a firewall for security.
Deny all traffic by default.
Permit only services that are needed.
Ensure that physical access to the firewall is controlled.
Regularly monitor firewall logs.
Practice change management for firewall configuration changes.
Remember that firewalls primarily protect from technical attacks originating from the outside.
Notes: 9: Firewall Technologies 9.2: Firewalls in Network Design 9.2.2: Layered Defense
9.2.3: Check Your Understanding – Identify Basic Security Architecture for Firewalls

## Slide 15
Module 10: Zone-Based Policy Firewalls
Networking Security v1.0
(NETSEC)
Notes: Networking Security (NETSEC) Module 10: Zone-Based Policy Firewalls

## Slide 16: Module Objectives
Module Title: Zone-Based Policy Firewalls
Module Objective: Implement Zone-Based Policy Firewall using CLI.
Topic Title | Topic Objective
ZPF Overview | Explain how Zone-Based Firewalls are used to help secure a network.
ZPF Operation | Explain the operation of a Zone-Based Policy Firewall.
Configuring a ZPF | Configure a Zone-Based Firewall with CLI.
Notes: 16
1 – Networking Today
1.0.2 – What will I learn to do in this module?

## Slide 17
10.1 ZPF Overview
Notes: 10: Zone-Based Policy Firewalls 10.1: ZPF Overview

## Slide 18
ZPF Overview
Benefits of a ZPF
There are two configuration models for Cisco IOS Firewall:
  Classic Firewall - The traditional configuration model in which firewall policy is applied on interfaces.
  Zone-based Policy Firewall (ZPF) - The new configuration mode in which interfaces are assigned to security zones, and firewall policy is applied to traffic moving between the zones.
There are several benefits of a ZPF:
  It is not dependent on ACLs.
  The router security posture is to block unless explicitly allowed.
  Policies are easy to read and troubleshoot with the Cisco Common Classification Policy Language (C3PL). C3PL is a structured method to create traffic policies based on events, conditions, and actions. This provides scalability because one policy affects any given traffic, instead of needing multiple ACLs and inspection actions for different types of traffic.
  Virtual and physical interfaces can be grouped into zones.
  Policies are applied to unidirectional traffic between zones.
Notes: 10: Zone-Based Policy Firewalls 10.1: ZPF Overview 10.1.1: Benefits of a ZPF

## Slide 19
ZPF Overview
ZPF Design
Designing ZPFs involves several steps:
  Step 1. Determine the zones. A zone defines a boundary where traffic is subjected to policy restrictions as it crosses to another region of the network.
  Step 2. Establish policies between zones. Define the sessions that clients in the source zones can request from servers in destination zones.
  Step 3. Design the physical infrastructure. This includes dictating the number of devices between most-secure and least-secure zones and determining redundant devices.
  Step 4. Identify subsets within zones and merge traffic requirements. Although an important consideration, implementing zone subsets is beyond the scope of this curriculum.
Notes: 10: Zone-Based Policy Firewalls 10.1: ZPF Overview 10.1.2: ZPF Design

## Slide 20
ZPF Overview
ZPF Design (Cont.)
LAN to Internet Example
Notes: 10: Zone-Based Policy Firewalls 10.1: ZPF Overview 10.1.2: ZPF Design

## Slide 21
ZPF Overview
ZPF Design (Cont.)
Firewall with Public Servers Example 1
Notes: 10: Zone-Based Policy Firewalls 10.1: ZPF Overview 10.1.2: ZPF Design

## Slide 22
ZPF Overview
ZPF Design (Cont.)
Firewall with Public Servers Example 2
Notes: 10: Zone-Based Policy Firewalls 10.1: ZPF Overview 10.1.2: ZPF Design

## Slide 23
ZPF Overview
ZPF Design (Cont.)
Redundant Firewalls
Notes: 10: Zone-Based Policy Firewalls 10.1: ZPF Overview 10.1.2: ZPF Design

## Slide 24
ZPF Overview
ZPF Design (Cont.)
Complex Firewall
Notes: 10: Zone-Based Policy Firewalls 10.1: ZPF Overview 10.1.2: ZPF Design

## Slide 25
10.2 ZPF Operation
Notes: 10: Zone-Based Policy Firewalls 10.2: ZPF Operation

## Slide 26
ZPF Operation
ZPF Actions
Policies identify actions that the ZPF will perform on network traffic. Three possible actions can be configured to process traffic by protocol, source and destination zones (zone pairs), and other criteria.
  Inspect - Performs Cisco IOS stateful packet inspection.
  Drop - Analogous to a deny statement in an ACL. A log option is available to log the rejected packets.
  Pass - Analogous to a permit statement in an ACL. The pass action does not track the state of connections or sessions within the traffic.
Notes: 10: Zone-Based Policy Firewalls 10.2: ZPF Operation 10.2.1: ZPF Actions

## Slide 27
ZPF Operation
Rules for Transit Traffic
Traffic transiting through router interfaces is subject to several rules governing interface behavior. For the transit traffic example, refer to the topology shown in the figure.
Source Interface Member of Zone? | Destination Interface Member of Zone? | Zone-Pair Exists? | Policy Exists? | Result
NO | NO | N/A | N/A | PASS
YES | NO | N/A | N/A | DROP
NO | YES | N/A | N/A | DROP
YES (private) | YES (private) | N/A | N/A | PASS
YES (private) | YES (public) | NO | N/A | DROP
YES (private) | YES (public) | YES | NO | DROP
YES (private) | YES (public) | YES | YES | INSPECT
Notes: 10: Zone-Based Policy Firewalls 10.2: ZPF Operation 10.2.2: Rules for Transit Traffic

## Slide 28
ZPF Operation
Rules for Traffic to the Self Zone
The self zone is the router itself and includes all the IP addresses assigned to the router interfaces. This is traffic that originates at the router or is addressed to a router interface.
The rules depend on whether the router is the source or the destination of the traffic, as shown in the table.
Source Interface Member of Zone? | Destination Interface Member of Zone? | Zone-Pair Exists? | Policy Exists? | Result
YES (self zone) | YES | NO | N/A | PASS
YES (self zone) | YES | YES | NO | PASS
YES (self zone) | YES | YES | YES | INSPECT
YES | YES (self zone) | NO | N/A | PASS
YES | YES (self zone) | YES | NO | PASS
YES | YES (self zone) | YES | YES | INSPECT
Notes: 10: Zone-Based Policy Firewalls 10.2: ZPF Operation 10.2.3: Rules for Traffic to the Self Zone
10.2.4: Check Your Understanding - Rules for Transit Traffic

## Slide 29
10.3 Configure a ZPF
Notes: 10: Zone-Based Policy Firewalls 10.3: Configure a ZPF

## Slide 30
Configure a ZPF
Configure a ZPF
The topology and steps shown in the figure will be used throughout the remainder of this topic to demonstrate ZPF configuration.
Step 1: Create the zones.
Step 2: Identify traffic with a class-map.
Step 3: Define an action with a policy-map.
Step 4: Identify a zone pair and match it to a policy-map.
Step 5: Assign zones to the appropriate interfaces.
https://www.cisco.com/c/en/us/support/docs/security/ios-firewall/98628-zone-design-guide.html
Notes: 10: Zone-Based Policy Firewalls 10.3: Configure a ZPF 10.3.1: Configure a ZPF

## Slide 31
Configure a ZPF
Step 1. Create Zones
The first step, is to create the zones. However, before creating the zones answer a few questions:
What interfaces should be included in the zones?
What will be the name for each zone?
What traffic is necessary between the zones and in which direction?
In the example topology, we have two interfaces, two zones, and traffic flowing in one direction. Traffic sourced from the public zone will not be allowed. Create the private and public zones for the firewall with the zone security command, as shown here.
PKT tracer: Router(config)#license boot module c2900 technology-package securityk9
Notes: 10: Zone-Based Policy Firewalls 10.3: Configure a ZPF 10.3.2: Step 1. Create Zones

## Slide 32
Configure a ZPF
Step 2. Identify Traffic
The second step is to use a class-map to identify the traffic to which a policy will be applied.
The figure shows the syntax for the class-map command. There are several types of class-maps. For a ZPF configuration, use the inspect keyword to define a class-map. Determine how packets are evaluated when multiple match criteria exist. Packets must meet one of the match criteria (match-any) or all of the match criteria (match-all) to be considered a member of the class.
Parameter | Description
match-any | Packets must meet one of the match criteria to be considered a member of the class.
match-all | Packets must meet all of the match criteria to be considered a member of the class.
class-map-name | Name of the class-map that will be used to configure the policy for the class in the policy-map.
Notes: 10: Zone-Based Policy Firewalls 10.3: Configure a ZPF 10.3.3: Step 2. Identify Traffic

## Slide 33
Configure a ZPF
Step 2. Identify Traffic (Cont.)
The figure shows the syntax for the match statements in class-map sub-configuration mode. Match traffic to an ACL, a specific protocol, or even another class-map.
Parameter | Description
match access-group | Configures the match criteria for a class-map based on the specified ACL number or name.
match protocol | Configures the match criteria for a class-map based on the specified protocol.
match class-map | Uses another class-map to identify traffic.
Notes: 10: Zone-Based Policy Firewalls 10.3: Configure a ZPF 10.3.3: Step 2. Identify Traffic

## Slide 34
In addition to user-defined classes, a system-defined class map named class-default represents all packets that do not match any of the user-defined classes in a policy. The class-default class is always the last class in a policy map.
You can define explicit actions for a group of packets that does not match any of the user-defined classes. If you do not configure any actions for the class-default class in an inspect policy, the default action is drop .
Configure a ZPF
Step 2. Identify Traffic - Class-Default Class Map (Cont.)

## Slide 35
Configure a ZPF
Step 3. Define an Action
The third step is to use a policy-map to define what action should be taken for traffic that is a member of a class. The figure shows the command syntax to configure a policy-map. An action is a specific functionality. It is typically associated with a traffic class. For example, inspect, drop, and pass are actions.
Parameter | Description
inspect | An action that offers state−based traffic control. The router maintains session information for TCP and UDP and permits return traffic.
drop | Discards unwanted traffic
pass | A stateless action that allows the router to forward traffic from one zone to another
Notes: 10: Zone-Based Policy Firewalls 10.3: Configure a ZPF 10.3.4: Step 3. Define an Action

## Slide 36
Configure a ZPF
Step 4. Identify a Zone-Pair and Match to a Policy
The fourth step is to identify a zone pair and associate that zone pair to a policy-map. The figure shows the command syntax. Create a zone-pair with the zone-pair security command. Then use the service-policy type inspect command to attach a policy-map and its associated action to the zone-pair.
Parameter | Description
source source-zone-name | Specifies the name of the zone from which traffic is originating.
destination destination-zone-name | Specifies the name of the zone to which traffic is destined.
self | Specifies the system-defined zone. Indicates whether traffic will be going to or from the router itself.
Notes: 10: Zone-Based Policy Firewalls 10.3: Configure a ZPF 10.3.5: Step 4. Identify a Zone-Pair and Match to a Policy

## Slide 37
Configure a ZPF
Step 5. Assign Zones to Interfaces
The fifth step is to assign zones to the appropriate interfaces. Associating a zone to an interface will immediately apply the service-policy that has been associated with the zone. If no service-policy is yet configured for the zone, all transit traffic will be dropped. Use the zone-member security command to assign a zone to an interface. In the example, GigabitEthernet 0/0 is assigned the PRIVATE zone, and Serial 0/0/0 is assigned the PUBLIC zone.
In the following example, GigabitEthernet 0/0 is assigned the PRIVATE zone, and Serial 0/0/0 is assigned the PUBLIC zone.
Notes: 10: Zone-Based Policy Firewalls 10.3: Configure a ZPF 10.3.6: Step 5. Assign Zones to Interfaces

## Slide 38
Configure a ZPF
Verify a ZPF Configuration
Verify a ZPF configuration by viewing the running configuration. Notice that the class-map is listed first. Then the policy-map makes use of the class-map.
The zone configurations follow the policy-map configurations with zone naming, zone pairing, and associating a service-policy to the zone pair.
Finally, the interfaces are assigned zones.
Notes: 10: Zone-Based Policy Firewalls 10.3: Configure a ZPF 10.3.7: Verify a ZPF Configuration

## Slide 39
Configure a ZPF
Verify a ZPF Configuration (Cont.)
The example shows verification information after a test of the ZPF configuration. A PRIVATE zone host 192.168.1.3 established an HTTPS session with a web server at 10.1.1.2. Notice further down in the command output that four packets matched the class class-default. This verification information was generated by having host 192.168.1.3 ping the web server at 10.1.1.2.
Other commands include:
show class-map type inspect
show zone security
show zone-pair security
show policy-map type inspect
Notes: 10: Zone-Based Policy Firewalls 10.3: Configure a ZPF 10.3.7: Verify a ZPF Configuration
10.3.8: Syntax Checker-Configure a ZPF

## Slide 40
Configure a ZPF
ZPF Configuration Considerations
When configuring a ZPF with the CLI, there are several factors to consider:
The router never filters the traffic between interfaces in the same zone.
An interface cannot belong to multiple zones. To create a union of security zones, specify a new zone and appropriate policy map and zone pairs.
ZPF can coexist with Classic Firewall although they cannot be used on the same interface. Remove the ip inspect interface configuration command before applying the zone-member security command.
Traffic can never flow between an interface assigned to a zone and an interface without a zone assignment. Applying the zone-member configuration command always results in a temporary interruption of service until the other zone-member is configured.
The default inter-zone policy is to drop all traffic unless otherwise specifically allowed by the service-policy configured for the zone-pair.
The zone-member command does not protect the router itself (traffic to and from the router is not affected) unless the zone- pairs are configured using the predefined self zone.
Notes: 10: Zone-Based Policy Firewalls 10.3: Configure a ZPF 10.3.9: ZPF Configuration Considerations